The Operating Manual for

DENON AV Receiver/Amplifier firmware update.

“DENON Flash Rom Writer Compact Version.”

| Model Name: | AVR-4806 |
| --- | --- |
| Version: | AVR-4806 : FWCV_AVR4806_V0004 |
| Date: | 2005-8-25 |

DENON

D&M Holdings, INC.

Index

1.	Preparations before starting the operation:	3

1.1	Preparation for the Personal Computer:	3

1.2	Preparations for the cables.	3

1.2.1	In case of updating using R-S232C connection.	3

1.2.2	In case of updating using Ethernet connection.	4

1.3	Connection diagram.	4

1.3.1	In case of updating using RS-232C connection.	4

1.3.2	In case of updating using Ethernet connection.	4

1.4	Install the DENON Flash ROM Writer Compact version.	5

2.	Firmware update procedure. (In case of updating using RS232C connection.).	6

2.1	Notice:	6

2.2	Set the AV Receiver/Amplifier into the firmware update mode.	6

2.3	Run the DENON Flash ROM Writer Compact version.	6

2.4	Communication check.	6

2.5	Start the firmware update.	7

2.6	Complete the firmware update.	7

3.	Firmware update procedure. (In case of updating using Ethernet connection.).	8

3.1	Notice:	8

3.2	In case of direct connection without hub using cross cable.	9

3.2.1	Setup the IP address PC and the AV Receiver/Amplifier	9

3.2.2	How to setup the fixed IP address of the AV Receiver/ Amplifier.	9

3.2.3	Power on the AV Receiver/Amplifier.	9

3.2.4	Run the DENON Flash ROM Writer Compact version.	10

3.2.5	Communication check.	10

3.2.6	Start the firmware update.	11

3.2.7	Complete the firmware update.	11

3.3	In case of Ethernet HUB or Router(without DHCP server ability)	12

3.3.1	Setup the IP address PC and the AV Receiver/Amplifier	12

3.3.2	How to setup the fixed IP address of the AV Receiver/ Amplifier.	12

3.3.3	Power on the AV Receiver/Amplifier.	12

3.3.4	Run the DENON Flash ROM Writer Compact version.	13

3.3.5	Communication check.	13

3.3.6	Start the firmware update.	14

3.3.7	Complete the firmware update.	14

3.4	In case of Router connection(with DHCP Server).	15

3.4.1	Setup the IP address PC and the AV Receiver/Amplifier	15

3.4.2	How to setup the auto IP address of the AV Receiver/Amplifier.	15

3.4.3	Power on the AV Receiver/Amplifier.	15

3.4.4	Confirm IP Address of the AV Receiver/Amplifier.	15

3.4.5	Run the DENON Flash ROM Writer Compact version.	16

3.4.6	Communication check.	16

3.4.7	Start the firmware update.	17

3.4.8	Complete the firmware update.	17

4.	Specific update mode.	18

# Preparations before starting the operation:

## Preparation for the Personal Computer:

Minimum hardware and software requirements:

| Type | PC/AT compatible |
| --- | --- |
| CPU | Intel Pentium/Celeron300MHz or faster |
| RAM | 128MB or more |
| Free hard disc space | 25MB or more |
| OS | Windows XP Home Edition / Professional SP1 or more |
| Display resolution | Super VGA (800x600) or more. |
| Port. | Serial COM port (D-Sub 9pin)[Recommendation] or ETHERNET port(RJ-45) |
| Communication speed | RS-232C:115,200bps ETHERNET:10BASE-T/100BASE-TX |

## Preparations for the cables.

### In case of updating using R-S232C connection.

Serial Straight Cable for RS-232C consisting of D-Sub 9P(female) and D-Sub 9P(female) cable.

D-Sub 9P(male) and D-Sub 9P(male) Gender Changer.

Note: There is the RS-232C(Male and Female) 9P cable like the following picture on the market. Then you don’t need to use Gender Changer.

However, Please confirm a nut part. If you can't remove the nut part, then you can't use this cable.

Because, AV Receiver/Amplifier RS-232C port also has the nut. You can not insert cable as physical conflict.

### In case of updating using Ethernet connection.

There are two methods.

- 10BASE-T/100BASE-TX Ethernet cross cable x 1pcs.

- 10BASE-T/100BASE-TX Ethernet straight cable x 2pcs
and 10BASE-T/100BASE-TX Ethernet HUB or Router.

## Connection diagram.

### In case of updating using RS-232C connection.

Connect the RS-232C cable between RS-232C port of PC and RS-232C port on rear panel of AV Receiver/Amplifier.

### In case of updating using Ethernet connection.

You can select the following 2 methods.

a) Connect the Ethernet cross cable between Ethernet port of PC and Ethernet port of AV Receiver/Amplifier.

b) Connect the Ethernet straight cable between Ethernet port of PC and Ethernet port of Hub (or Router). And connect the Ethernet straight cable between Ethernet port of Hub (or Router) and Ethernet port of AV Receiver/Amplifier.

## Install the DENON Flash ROM Writer Compact version.

- Execute the“FWCV_AVR4806_V0004_SETUP.exe”or the“FWCV_AVCA11XV_V0004_SETUP.exe”.

- Install utility according to message.

- After installed, you can see the‘DENON FWCV_AVR4806_V0004’icon 
or the‘DENON FWCV_AVCA11XV_V0004’icon on desktop.

# Firmware update procedure. (In case of updating using RS232C connection.).

## Notice:

Please keep the following notice for firmware update.

a) Keep the PC environment refer to 1.1.

b) Avoid the communication cable from the electrical noise source.
(e.g. telephone cable, AC line, a fluorescent light)

c) Don’t remove cable during update.

d) Don’t turn off the power during update.

e) Don’t run other PC application during update.

f) Stop the resident program on PC.

g) Stop the screen saver ability on PC.

h) Stop the power save ability on PC.

i) In case of laptop PC, Use the AC adaptor.

## Set the AV Receiver/Amplifier into the firmware update mode.

Operate the following. The AV Receiver/ Amplifier goes to the firmware update mode.

1) Turn on the power switch of the AV Receiver/Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power indicator green pushing the ON/STANDBY button.

## Run the DENON Flash ROM Writer Compact version.

Run the‘DENON FWCV_AVR4806_V0004’or the‘DENON FWCV_AVCA11XV_V0004’on desktop of PC.

## Communication check.

1) Select the ”RS-232C”.

2) Select the serial port number of PC.

3) Click the “Check communication” button.

4) If connection is good, then you can see the“Communication check OK.”message.

5) Please wait 1 min at least. If connection is not good, then you can see the“Communication check NG!” message. 

Please confirm the following. 
a) Check the connection (refer to 1.3.1).

b) Check the firmware update mode status (refer to 2.2).

c) Check the port number of PC (refer to 2.4(2)).

## Start the firmware update.

Click the“Update” button.

## Complete the firmware update.

1) When Update utility completed the firmware update, you can see the“Update completed.”message.

2) If you can’t complete the firmware update, please retry the firmware update from 2.2. 
However, If you failed update during Main CPU update, then you need to use a specific update procedure (refer to 4).

# Firmware update procedure. (In case of updating using Ethernet connection.).

If you use the Ethernet update, then you need to have network knowledge.

If you don’t have network knowledge, then please use RS232C connection.

## Notice:

Please keep the following notice for firmware update.

a) Keep the PC environment refer to 1.1.

b) Avoid the communication cable from the electrical noise source.
(e.g. telephone cable, AC line, a fluorescent light)

c) Don’t remove cable during update.

d) Don’t turn off the power during update.

e) Don’t run other PC application during update.

f) Stop the resident program on PC.

g) Stop the screen saver ability on PC.

h) Stop the power save ability on PC.

i) In case of laptop PC, Use the AC adaptor.

## In case of direct connection without hub using cross cable.

### Setup the IP address PC and the AV Receiver/Amplifier

Setup the IP Address.

1) Setup the fixed IP address of PC.
IP Address:192.168.0.2, Subnet Mask:255.255.255.0

2) Setup the fixed IP address of the AV Receiver/Amplifier. 
Refer to 3.2.2. 
IP Address:192.168.0.1, Subnet Mask: 255.255.255.0

### How to setup the fixed IP address of the AV Receiver/ Amplifier.

1) Keep to push the‘STANDARD’button and the‘INPUT MODE’button on the AV Receiver/Amplifier simultaneously. And turn on the power switch of 
the AV Receiver /Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power indicator green pushing the ON/STANDBY button.

3) Push the ‘SYSTEM SETUP’ button. You can see the “System Setup” menu.

4) Select the “Option Setup” using cursor UP/DOWN button.

5) Push the “CH SEL ENTER” button. Select the "Network Setup" using cursor UP/DOWN button.

6) Push the “CH SEL ENTER” button. You can see the "IP Address".

7) Push the “CH SEL ENTER” button. Setup the "DHCP : < ON >" to <OFF> using cursor LEFT/RIGHT button.

8) Push the cursor DOWN button. Push the cursor RIGHT button at “IP Address” indication.

9) Setup the IP Address using cursor LEFT/RIGHT/UP/DOWN button. 
Push the “CH SEL ENTER”. Then set the IP address.

10) Also, Setup the "Subnet Mask".

11) Finish the “System Setup” using the  “SYSTEM SETUP” button.

### Power on the AV Receiver/Amplifier.

It is not necessary using the firmware update mode.

1) Turn on the power switch of the AV Receiver/Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power
indicator green pushing the ON/STANDBY button.

### Run the DENON Flash ROM Writer Compact version.

Run the‘DENON FWCV_AVR4806_V0004’or the‘DENON FWCV_AVCA11XV_V0004’on desktop of PC.

### Communication check.

1) Select the “Ethernet”.

2) Input the IP Address.

3) Click the “Check Communication” button.

4) If connection is good, You can see the “Communication check OK.” Message.

5) Please wait 1 min at least. If connection is not good, then you can see
 the“Communication check NG!”message. 

Please confirm the following. 
a) Check the connection (refer to 1.3.2(a)).
b) Check Power on Mode (refer to 3.2.3).

b) Check the IP address (refer to 3.2.5(2)).

### Start the firmware update.

Click the “Update” button.

### Complete the firmware update.

1) When Update utility completed the firmware update, you can see the “Update completed.”message.

2) If you can’t complete the firmware update, please retry the firmware update from 3.3. 
However, If you failed update during Main CPU update, then you need to use a specific update procedure (refer to 4).

## In case of Ethernet HUB or Router(without DHCP server ability)

### Setup the IP address PC and the AV Receiver/Amplifier

Setup the IP Address.

1) Setup the fixed IP address of PC.
IP Address:192.168.0.2, Subnet Mask:255.255.255.0

2) Setup the fixed IP address of the AV Receiver/Amplifier. 
Refer to 3.3.2. 
IP Address:192.168.0.1, Subnet Mask: 255.255.255.0

### How to setup the fixed IP address of the AV Receiver/ Amplifier.

1) Keep to push the‘STANDARD’button and the‘INPUT MODE’button on the AV Receiver/Amplifier simultaneously. And turn on the power switch of 
the AV Receiver /Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power indicator green pushing the ON/STANDBY button.

3) Push the ‘SYSTEM SETUP’ button. You can see the “System Setup” menu.

4) Select the “Option Setup” using cursor UP/DOWN button.

5) Push the “CH SEL ENTER” button. Select the "Network Setup" using cursor UP/DOWN button.

6) Push the “CH SEL ENTER” button. You can see the "IP Address".

7) Push the “CH SEL ENTER” button. Setup the "DHCP : < ON >" to <OFF> using cursor LEFT/RIGHT button.

8) Push the cursor DOWN button. Push the cursor RIGHT button at “IP Address” indication.

9) Setup the IP Address using cursor LEFT/RIGHT/UP/DOWN button. 
Push the “CH SEL ENTER”. Then set the IP address.

10) Also, Setup the "Subnet Mask".

11) Finish the “System Setup” using the  “SYSTEM SETUP” button.

### Power on the AV Receiver/Amplifier.

It is not necessary using the firmware update mode.

1) Turn on the power switch of the AV Receiver/Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power
indicator green pushing the ON/STANDBY button.

### Run the DENON Flash ROM Writer Compact version.

Run the‘DENON FWCV_AVR4806_V0004’or the‘DENON FWCV_AVCA11XV_V0004’on desktop of PC.

### Communication check.

1) Select the “Ethernet”.

2) Input the IP Address.

3) Click the “Check Communication” button.

4) If connection is good, You can see the “Communication check OK.” Message.

5) Please wait 1 min at least. If connection is not good, then you can see
 the“Communication check NG!”message. 

Please confirm the following. 
a) Check the connection (refer to 1.3.2(b)).
b) Check Power on Mode (refer to 3.3.3).

b) Check the IP address (refer to 3.3.5(2)).

### Start the firmware update.

Click the “Update” button.

### Complete the firmware update.

1) When Update utility completed the firmware update, you can see the “Update completed.”message.

2) If you can’t complete the firmware update, please retry the firmware update from 3.3.3. 
However, If you failed update during Main CPU update, then you need to use a specific update procedure (refer to 4).

## In case of Router connection(with DHCP Server).

### Setup the IP address PC and the AV Receiver/Amplifier

Setup the IP Address at Auto IP mode.

1) Setup the auto IP address of PC.

2) Setup the auto IP address of the AV Receiver/Amplifier. 
Refer to 3.4.2.

### How to setup the auto IP address of the AV Receiver/Amplifier.

1) Keep to push the‘STANDARD’button and the‘INPUT MODE’button on the AV Receiver/Amplifier simultaneously. And turn on the power switch of 
the AV Receiver/Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power indicator green pushing the ON/STANDBY button.

3) Push the ‘SYSTEM SETUP’ button. You can see the “System Setup” menu.

4) Select the “Option Setup” using cursor UP/DOWN button.

5) Push the “CH SEL ENTER” button. Select the "Network Setup" using cursor UP/DOWN button.

6) Push the “CH SEL ENTER” button. You can see the "IP Address".

7) Push the “CH SEL ENTER” button. Setup the "DHCP : < OFF >" to <ON> using cursor LEFT/RIGHT button.

8) Finish the “System Setup” using the  “SYSTEM SETUP” button.

### Power on the AV Receiver/Amplifier.

Operate the following. The AV Receiver/ Amplifier goes to the network setting mode.

1) Keep to push the‘STANDARD’button and the‘INPUT MODE’button on the AV Receiver/Amplifier simultaneously. And turn on the power switch of
the AV Receiver/Amplifier.

2) Confirm the power indicator is green. If the power indicator is red, Make the power indicator green pushing the ON/STANDBY button.

### Confirm IP Address of the AV Receiver/Amplifier.

Operate the following. Confirm IP Adress of the AV Receiver/Amplifier.

1) Push the‘SYSTEM SETUP’button. You can see the “System Setup” menu.

2) Select the “Option Setup” using cursor UP/DOWN button.

3) Push the “CH SEL ENTER” button. Select the "Network Setup" using cursor UP/DOWN button.

4) Push the “CH SEL ENTER” button. You can see the "IP Address".

5) Push the “CH SEL ENTER” button. You can see the "DHCP : < ON >" .

6) Push the cursor DOWN button. You can confirm the IP Address.

7) Finish the “System Setup” using the “SYSTEM SETUP” button.

### Run the DENON Flash ROM Writer Compact version.

Run the‘DENON FWCV_AVR4806_V0004’or the‘DENON FWCV_AVCA11XV_V0004’on desktop of PC.

### Communication check.

1) Select the “Ethernet”.

2) Input the IP Address (refer to 3.2.6).

3) Click the “Check Communication” button.

4) If connection is good, You can see the “Communication check OK.” Message.

5) Please wait 1 min at least. If connection is not good, then you can see the “Communication check NG!” message. 

Please confirm the following. 
a) Check the connection (refer to 1.3.2(b))
b) Check Power on Mode (refer to 3.4.3).
b) Check the IP address (refer to 3.4.5(2)).

### Start the firmware update.

Click the “Update” button.

### Complete the firmware update.

1) When Update utility completed the firmware update, you can see the “Update completed.”message.

2) If you can’t complete the firmware update, please retry the firmware update from 3.4.3. 
However, If you failed update during Main CPU update, then you need to use a specific update procedure (refer to 4).

# Specific update mode.

If you failed update during Main CPU update, then you need to use this specific update procedure.

1) The AV Receiver/Amplifier is connected with PC with the RS-232C cable. Refer to 1.3.1.

2) Push the ‘SURROUND PARAMETER’+‘SURROUND BACK’button simultaneously.
And turn on the power switch of the AV Receiver/Amplifier.

3) Power indicator indicates red color. This is specific update mode.

4) Please execute the firmware update. Refer to 2.3.

# Text boxes

(2)

(3)

(1)

(2)

Gender Changer

D-Sub 9P(male) and D-Sub 9P(male)

D-Sub 9P(female) and D-Sub 9P(female) cable

(3)

(2)

(1)

(3)

(2)

(1)

RS-232C

Straight cable.

AV Receiver /Amplifier.

PC

Rear Panel

Ethernet cross cable

AV Receiver /Amplifier.

PC

Ethernet
straight
cable

Ethernet
straight
cable

HUB
or
Router

AV Receiver /Amplifier.

PC

(1)

(3)

DENON FWCV_AVR48

06_V0004

DENON FWCV_AVR48

06_V0004

DENON

FWCV_AVR48

06_V0004

DENON

FWCV_AVR48

06_V0004

DENON

FWCV_AVR48

06_V0004